These equations let you size a single stage craft and find the payload (if any) for a given mission profile (dV, TMR)

T = {F cdot ( 1-e^{-%DELTA V/V_e} )} over { TMR cdot (R-1) } newline P = { F } over { TMR } - E - R cdot T

And these equations determine the optimum (maximum dV) fuel split between two stages. Note that these do not account for TMR requirements.

a = -V_el T^2 R (R-1) newline b = T(E_u+P)(V_eu(R-1)^2-V_el(R+1)(R-1)) newline c = V_eu(R-1)(E_u+P)(E_u+E_l+T+P+S)-V_el(R-1)(E_u+P)^2 newline newline x = {-b+sqrt{b^2 - 4ac}} over {2a}

Variable(s)	Meaning
dV	Change in velocity (“delta-vee”)
E	Engine mass (single stage)
Eu	Engine mass (upper stage)
El	Engine mass (lower stage)
F	Maximum thrust (“force”)
P	Payload mass
R	Mass ratio of tankage. 9 for most stock rocket tanks, 8 for Mk2/3 fuselages.
S	Extra stage mass (the penalty from having a stage, typically a decoupler).
T	Tankage mass (dry)
TMR	Thrust to Mass Ratio (N/kg or m/s2)
Ve	Effective exhaust velocity (9.80665 m/s2 * Isp in s),
Vel	Effective exhaust velocity of the lower stage
Veu	Effective exhaust velocity of the upper
x	Fraction of tankage mass in the upper stage
1-x	Fraction of tankage mass in lower stage
RT	Fully fuelled tankage mass.
Tx	Upper stage empty tankage mass
RTx	Upper stage fully fuelled tankage mass
T(1-x)	Lower stage empty tankage mass
RT(1-x)	Lower stage fully fuelled tankage mass